## Slide 1: 19ECE204 Digital Electronics and Systems III Semester B. Tech. (ECE & CSE) Amrita School of Engineering, Bengaluru
Synchronous Sequential Circuits

## Slide 3: Sequential Circuits
We considered combinatorial logic circuits in which outputs are fully determined by the present values of the inputs.
We also considered simple storage elements that can be implemented in the form of flipflops for which the output depends on their states rather than the value of the inputs; the inputs cause changes in the state.
In this lecture we deal with a general class of circuits in which the output depend on the past behavior of the circuit, as well on the present values of the inputs.
They are called sequential circuits.

## Slide 4: Synchronous vs Asynchronous
In most cases a clock signal is used to control the operation of a sequential circuit.Such circuit is called synchronous.
• The alternative, in which clock signal is not used, is called asynchronous sequential circuits.
• Synchronous circuits are easier to design and are used in the vast majority of practical applications.

## Slide 16: State Diagram

## Slide 17: State Table

## Slide 18: State Table

## Slide 19: State Assignment(1)

## Slide 22
State Assignment(4)

## Slide 33: Mealy state model

## Slide 34: Mealy state model
Sequence of input –output & State Diagram

## Slide 35
State TABLE for FSM
State ASSIGNED TABLE for FSM

## Slide 36: Circuit for Mealy FSM

## Slide 41: Sequential Circuit Design
Understand specifications
Draw state graph (to describe state machine behavior)
Construct state table (from state graph)
Perform state minimization (if necessary)
Encode states (aka. state assignment)
Create state-assigned table
Select type of Flip-Flop to use
Determine Flip-Flop input equations and FSM output equation(s)
Draw logic diagram

## Slide 42: Example: A sequence detector (Mealy)
To illustrate the design of a clocked Mealy sequential circuit, we will design a sequence detector.
The circuit is of the form:
serial bit stream (input)
output (serial bit stream)

## Slide 43: Example: A sequence detector (Mealy)
Suppose we want to design the sequence detector so that any input sequence ending in 101 will produce an output of Z = 1 coincident with the last 1.
The circuit does not reset when a 1 output occurs.
A typical input sequence and the corresponding output sequence are:
X = 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 0
Z = 0 0 0 0 0 1 0 0 0 0 0 1 0 1 0 0
(time: 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15)

## Slide 44: Example: A sequence detector (Mealy)
Initially, we do not know how many flip-flops will be required, so we will designate the circuit states as S0, S1, etc.
We will start with a reset state designated S0.
If a 0 input is received, the circuit can stay in S0 because the input sequence we are looking for does not start with a 0.

## Slide 45: Example: A sequence detector (Mealy)
State Graph for the Mealy Machine

## Slide 46: Example: A sequence detector (Mealy)
We can then convert our state graph to a state table:
Since there are 3 states, we only need 2 flip-flops for the circuit.

## Slide 47: Example: A sequence detector (Mealy)
And then convert our state table to a transition table:

## Slide 48: Example: A sequence detector (Mealy)
From the transition table, we can plot the next-state maps for the flip-flops and the map for the output function Z:

## Slide 49: Example: A sequence detector (Mealy)
Using the derived equations, we can then draw the corresponding circuit diagram:

## Slide 50: Example: A sequence detector (Moore)
State Graph for the Moore Machine

## Slide 51: Example: A sequence detector (Moore)
As with the Mealy machine, the state and transition tables can be derived from the state graph:

## Slide 52: Revision

## Slide 56: Counter Design

## Slide 57
Figure 8.60. State diagram for the counter.
w
0
=
w
1
=
w
0
=
w
1
=
w
0
=
w
1
=
w
0
=
w
1
=
w
0
=
w
1
=
w
0
=
w
1
=
w
0
=
w
1
=
w
0
=
w
1
=
A/0
B/1
C/2
D/3
E/4
F/5
G/6
H/7

## Slide 58
Figure 8.61. State table for the counter.
Present
Next state
Output
state
w
=
0
w
=
1
A
A
B
0
B
B
C
1
C
C
D
2
D
D
E
3
E
E
F
4
F
F
G
5
G
G
H
6
H
H
A
7

## Slide 59
Figure 8.62. State-assigned table for the counter.
Present
Next state
state
w
=
0
w
=
1
Count
y
2
y
1
y
0
Y
2
Y
1
Y
0
Y
2
Y
1
Y
0
z
2
z
1
z
0
A
000
000
001
000
B
001
001
010
001
C
010
010
011
010
D
011
011
100
011
E
100
100
101
100
F
101
101
110
101
G
110
110
111
110
H
111
111
000
111

## Slide 60
Figure 8.63. Karnaugh maps for D flip-flops for the counter.
00
01
11
10
00
01
1
0
1
1
1
0
0
0
0
1
0
0
0
1
1
1
11
10
y
1
y
0
wy
2
00
01
11
10
00
01
0
0
0
1
1
1
1
0
1
0
1
0
0
1
1
0
11
10
y
1
y
0
wy
2
00
01
11
10
00
01
0
1
1
0
1
0
1
0
1
0
0
0
1
1
0
1
11
10
y
1
y
0
wy
2
D
2
wy
2
y
0
y
2
y
1
y
2
w
+
+
+
y
0
y
1
y
2
=
D
0
wy
0
wy
0
+
=
D
1
wy
1
y
1
y
0
wy
0
y
1
+
+
=

## Slide 61
D
Q
Q
D
Q
Q
Clock
y
0
w
y
1
y
2
Y
0
Y
1
Y
2
Resetn
D
Q
Q
Figure 8.64. Circuit diagram for the counter implemented
with D flip-flops.

## Slide 64: ALL THE BEST